## Slide 1: HPMP and Its Impact on HCFCs in INDIA
by Richie Mittal, ISHRAE
Richie Mittal

## Slide 2
Montreal Protocol
HPMP ( HCFC Phase Out)
Impact on HVAC&R
ISHRAE’s Role
Agenda
Richie Mittal

## Slide 3: The Montreal Protocol
The Montreal Protocol is a response to the global nature of ozone depletion.
On September 16, 1987, in Montreal, 24 nations and the European Economic Community (EEC) signed the Montreal Protocol on substances that deplete the ozone layer.
Most of the nations that are major producers and consumers of CFCs and halon signed the agreement.
Richie Mittal

## Slide 4: The Montreal Protocol (continued)
Figure 2-4. The ozone depletion process.
Richie Mittal

## Slide 5: Montreal Protocol
India became party > 17th September 1992
CFC Phase-out > 1st Aug 2008 for RAC
HCFC Phase-out
  Base-level for production & consumption: the avg of 2009 and 2010.
  Freeze=2013 at the base-level
  10% reduction in 2015
  35% reduction in 2020
  67.5% reduction in 2025
  100% reduction in 2030 allowing for servicing an annual average of 2.5% during the period 2030-2040.
Richie Mittal

## Slide 6: Accelerated phase-out of HCFCs
In September 2007, the Parties to the Montreal Protocol agreed to accelerate the phase-out of HCFCs, bringing the final phase-out date forward by 10 years for Developed and Developing countries.
Baseline = average ODP weighted 2009, 2010 HCFC consumption
Richie Mittal

## Slide 7: Applications impacted
Refrigerants
Foams
Fire
Solvent (cleaning etc)
Richie Mittal

## Slide 8: Calculation of Base Line
Base Line eg India
ODP T = MT X ODP
 |  | MT |  |  | ODP T |  | 
HCFC | ODP | 2009 | 2010 | Baseline | 2009 | 2010 | Baseline
HCFC-123 | 0.020 | 238 | 115 | 176.5 | 4.76 | 2.3 | 3.53
HCFC-124 | 0.022 | 620 | 603 | 611.5 | 13.64 | 13.27 | 13.46
HCFC-141b | 0.11 | 7900 | 7837 | 7868.5 | 869 | 862.07 | 865.54
HCFC-142b | 0.065 | 3001 | 805 | 1903 | 195.07 | 52.33 | 123.7
HCFC-22 | 0.055 | 9387 | 12503 | 10945 | 516.29 | 687.67 | 601.98
Total |  | 21146 | 21863 | 21504.5 | 1598.76 | 1617.64 | 1608.2
Richie Mittal

## Slide 9: Calculation of Base Line
Base Line eg India
ODP T = MT X ODP
 |  | ODP T |  | 
HCFC | ODP | 2009 | 2010 | Baseline
HCFC-123 | 0.020 | 4.76 | 2.3 | 3.53
HCFC-124 | 0.022 | 13.64 | 13.27 | 13.46
HCFC-141b | 0.11 | 869 | 862.07 | 865.54
HCFC-142b | 0.065 | 195.07 | 52.33 | 123.7
HCFC-22 | 0.055 | 516.29 | 687.67 | 601.98
Total |  | 1598.76 | 1617.64 | 1608.2
62.3% of Baseline
Richie Mittal

## Slide 10: HCFC 22 and HCFC 123
Start of Impact
Richie Mittal

## Slide 11: Alternatives
R22
R410A
R32
R290
Others
R123
R134a
HCFO 1233zd
HFO 1336mzz
Flammable
Richie Mittal

## Slide 12: ISHRAE’s Role
Refrigerants Technical Committee
Dec 2015 release of Position paper
Nov 2017 release of Guidelines for safe
and sustainable use of Refrigerants
Participating in stakeholders workshops
BEE and BIS support
Richie Mittal

## Slide 13: Refrigerant Trainings 2017
Full day training programs on Refrigerants
  Nasik, Kolhapur, Sangli, Ludhiana, Karad, Satara
Half day or short talks many more
Webinars on Refrigerant
  Basics of Refrigerants
  Impact of Montreal Protocol
Videos by DL on Member Login
  Basics of Refrigerants
  Safety Regulations and Indian Scenario
1500+
Individuals covered
Richie Mittal

## Slide 14
Thank You
Upcoming Webinar:
Alternative Refrigerants and Evaluation Indian Context
Richie Mittal